## Slide 1: Coronagraph Rapid Imaging Spectrograph in Python (CRISPY)
Maxime Rizzo, Tyler Groff, Neil Zimmerman & Goddard IFS Lab,
Ewan Douglas (MIT/Cahoy Lab)
WFIRST Data Analysis Group Presentation
Feb 2nd, 2017

## Slide 2: What’s CRISPY?
A software suite that can simulate the WFIRST Integral Field Spectrograph
Can be used in conjunction with a Coronagraph PSF model for end-to-end simulation
  3D Science scenes -> extracted data cubes

## Slide 3: Integral Field Spectrograph
Lenslet sampling is based on size of telescope
“PSFLet”: PSF for each lenslet spectrum measured on the detector

## Slide 4: WFIRST IFS
Major Contributions
  On-orbit wavefront control
  Low spectral crosstalk
  Passive speckle suppression
Major Objectives
  Demonstrate on-orbit spectral characterization of exoplanets
  IWA = 3 λ/D
  OWA = 10 λ/D
  R50, 600-970nm
Basic Parameters
  R50, 3 bands spanning 600-970 nm
  2 lenslets per λ/D
  Photon counting EMCCD

## Slide 5: WFIRST IFS Optics
Current bandpasses (600-970nm) allow for refractive design
First CaF2 optic reduces size of relay elements
  Unique to the PISCES and WFIRST designs
  Minimizes wavefront error at each field point
  Cost: non-common wavefront across the FOV
PISCES Optical Design
Current Flight Analog

## Slide 6: Purpose of CRISPY
Distribute to community to test extraction routines
  “Toy” model
Use internally for flight IFS tradeoffs & sensitivity analysis

## Slide 7: Software layout
Haystacks
Generate broadband cube
w/ POPPY CGI model(s) or JPL PROPER model
Propagate through IFS
Generate detector map
Add noise sources
Data reduction pipeline
Post-processing/extraction
Wavelength calibration
and update
Realistic calibration fields
Astrophysical
Scene
Diffractive
Propagation
Semi-Empirical IFS convolution
CCD behavior models

## Slide 8: Haystacks
Realistic models of extrasolar systems led by A. Roberge
  Local and exo-zodiacal dust
  Modeled planetary spectra
  Background stars & galaxies
  Broad wavelength range
  Can even model moons around planets!
Code already has a few existing self-consistent architectures
  Solar system twin
  ‘Endor’ system with Jupiter-like planet and Earth-like moon
  Can vary inclination angle, distance, sampling, zodis, etc

## Slide 9: Haystacks cube for WFIRST filter
Solar system cube seen face-on at 5pc

## Slide 10: Input scene parsing
Sample at 4x diffraction limit (0.01425”).
Generate tilted wavefronts for each wavelength from relatively bright (i.e. >5e-11 contrast) sources in scene
Apply webbpsf Fraunhofer SPC model (currently testing Fresnel domain model)
Sum post-coronagraph electric field intensities
Record same-color on-axis reference target diffraction pattern
  Store as wavelength vs. intensity cube
  Document instrument configuration and model choices in in FITS header
Future:
Add approximation of (post-correction) wavefront error
Full wavelength coverage
Library of PSFs vs. all angles for rapid reconstruction of new scenes

## Slide 11: POPPY simulations

## Slide 12: IFS propagation
Remap each slice of input cube onto lenslet array
  1 square portion of scene = 1 square lenslet
For each lenslet and wavelength, determine X Y location in detector plane using polynomial function of (X,Y,λ)
Add oversampled PSFlet on oversampled detector plane at correct position
Rebin onto final detector sampling

## Slide 13: Example
Cube of inputs to the IFS
IFS detector map
Optimal extraction
Least-squares extraction

## Slide 14: Detector noise: approach
Deliver software with standard Gaussian/Poisson noise sources
Work on implementation of noise specific to EMCCDs
Work with JPL/MIT on Python implementation of traps sims for the future

## Slide 15: Traps code example
Traps code from JPL/Bijan Nemati

## Slide 16: IFS wavelength calibration
Generate monochromatic flatfields to determine wavelength/pixel relationship for each lenslet spectrum
Optimization routine to fit polynomial function to lenslet positions for each wavelength
From PSFLet ‘diversity’ across the field, generate high-resolution simulated PSFLets in different regions of the image; equivalent to assuming we have very good knowledge of PSFLets
Create ‘polychrome’ cubes with model PSFLets at all the correct locations

## Slide 17: CHARIS: Impact of Image Registration
Update
No
Update

## Slide 18: Wavelength calibration update
Able to test in-flight calibration correction scenarios -> inform flight observing requirements, stability tolerances, etc
Implementing CHARIS single-wavelength update strategy, but investigating other possibilities

## Slide 19: Data reduction pipeline
Using Tim Brandt/CHARIS DRP framework
  Optimal extraction
  Least-squares fitting with prior knowledge of PSFLets (using the polychrome cube)
Implementing GPI and other methods as well for comparison
Fully compatible and tested with PISCES testbed at HCIT

## Slide 20: WFIRST Wavefront Control on-orbit
For WFIRST we must achieve contrasts of ~1x10-9 in the IFS
Necessitates digging a dark hole with the IFS itself
The IFS must auto-reduce data cubes on-orbit
  Efficient Dark Holes
  Sensitive to Alignment Errors in the IFS
Stability of the IFS is key to success
  Misalignment of spectrograph
  Misalignment of image on detector
Design Approach
  Demonstrate stability of the spectrograph
  Be able to calibrate image registration
Reduced Image from PISCES demonstrator
Raw IFS Image with monochromatic Dark Hole

## Slide 21: PISCES example

## Slide 22: Post-processing
Expected to add a simple module for extraction methods such as KLIP
Open to suggestions and assistance

## Slide 23: Goddard IFS team planned trade-offs
Sensitivities of reduced cube on various IFS parameters:
  PSF sampling at detector
  Effective spectral resolution (# pixels vs resolving power)
  Data extraction method
  Accuracy of wavelength calibration
  Orientation of dispersion direction with respect to serial readout

## Slide 24: Status
All essential elements working
  Need to establish benchmarks and sanity checks
Currently proof-reading, writing unit tests, writing docs & notebooks
Need to implement a few more routines:
  Wavelength calibration updates
Detector noise
Will add post-processing module